## Slide 1: CSC 322: Computer Organization Lab
Logic Design
Dr. Haidar M. Harmanani

## Slide 2: Part I: Bits and Bytes

## Slide 3: Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as
      0xFA1D37B
      0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary
15213: 0011 1011 0110 1101
3
B
6
D

## Slide 4: Example Data Representations
C Data Type | Typical 32-bit | Typical 64-bit | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8

## Slide 5: General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 6: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 → 0xBE
    ~010000012 → 101111102
  ~0x00 → 0xFF
    ~000000002 → 111111112
  0x69 & 0x55 → 0x41
    011010012 & 010101012 → 010000012
  0x69 | 0x55 → 0x7D
    011010012 | 010101012 → 011111012
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 7: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 → 0xBE
    ~0100 00012 → 1011 11102
  ~0x00 → 0xFF
    ~0000 00002 → 1111 11112
  0x69 & 0x55 → 0x41
    0110 10012 & 0101 01012 → 0100 00012
  0x69 | 0x55 → 0x7D
    0110 10012 | 0101 01012 → 0111 11012
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 8: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
      Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on left
Undefined Behavior
  Shift amount < 0 or ≥ word size
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000

## Slide 9: Encoding Integers
short int x = 15213;
short int y = -15213;
C short 2 bytes long
Sign Bit
  For 2’s complement, most significant bit indicates sign
    0 for nonnegative
    1 for negative

## Slide 10: Two-complement: Simple Example
10 =
-16 | 8 | 4 | 2 | 1
0 | 1 | 0 | 1 | 0
-10 =
-16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 1 | 0
8+2 = 10
-16+4+2 = -10

## Slide 11: Numeric Ranges
Values for W = 16
Unsigned Values
  UMin = 0
    000…0
  UMax = 2w – 1
    111…1
Two’s Complement Values
  TMin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
  Minus 1
    111…1

## Slide 12: Mapping Between Signed & Unsigned
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X
U2T
U2B
B2T
Two’s Complement
Unsigned
Maintain Same Bit Pattern
ux
x
X
Mappings between unsigned and two’s complement numbers: Keep bit representations and reinterpret

## Slide 13: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
U2T
T2U

## Slide 14: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
=
+/- 16

## Slide 15: Relation between Signed & Unsigned
+
+
+
+
+
+
• • •
-
+
+
+
+
+
• • •
ux
x
w–1
0
Large negative weight
becomes
Large positive weight
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X

## Slide 16: Signed vs. Unsigned in C
Constants
  By default are considered to be signed integers
  Unsigned if have “U” as suffix
    0U, 4294967259U
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and procedure calls
    tx = ux; int fun(unsigned u);
    uy = ty; uy = fun(tx);

## Slide 17: Unsigned vs. Signed: Easy to Make Mistakes
    unsigned i;
    for (i = cnt-2; i >= 0; i--)
    a[i] += a[i+1];

## Slide 18: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 19: Sign Extension: Simple Example
10 =
-16 | 8 | 4 | 2 | 1
0 | 1 | 0 | 1 | 0
10 =
-32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 1 | 0 | 1 | 0
-10 =
-16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 1 | 0
-32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 1 | 1 | 0
-10 =
Positive number
Negative number

## Slide 20: Larger Sign Extension Example
Converting from smaller to larger integer data type
C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 21: Part II: Transistors, Switches, and Gates

## Slide 22: Technology Review
CMOS “Complementary Metal Oxide Semiconductor”
  Presently prevalent chip technology
14nm CMOS cross section
14nm CMOS top view

## Slide 23: 5nm Transistor
Source: Intel press foils
Transistor is < 100 atoms across!

## Slide 24: Transistors for building Logic
To a computer, everything is 1’s and 0’s
In electronic circuits we represent 1’s and 0’s with voltages. E.g.
  1  1V (5V works too, but consumes more power)
  0  0V
Questions:
  What is 0.9V?
  What is 0.2V? How about 0.5?

## Slide 25: Everything is bits
Each bit is 0 or 1
By encoding/interpreting sets of bits in various ways
  Computers determine what to do (instructions)
  … and represent and manipulate numbers, sets, strings, etc…
Why bits? Electronic Implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.2V
0.9V
1.1V
0
1
0

## Slide 26: MOS Transistor Operation
Silicon
Control Terminal
Metal
Oxide
Semiconductor
0V
Transistor:
Model (switch):
A
B
A
B
C = 0V  switch open (no current flows between A and B)
C
1V
C = 1V  switch closed (current can flow between A and B)
Yes, this is simplistic. If you cringe, you do not need this explanation. Stick with what you know already.
Notes: C=0V: no electrons  no current can flow. Like railway with only rails but no trains.
C=1V sucks electrons up to the surface  current can flow, “carried” by the electrons.

## Slide 27: CMOS Complementary Metal Oxide Semiconductor
NMOS Transistor (= Switch)
Switch closed for C = 1V (“1”)
open for C = 0V
PMOS Transistor (= Switch)
Switch closed for C = 0V (“0”)
open for C = 1V
A
B
C
A
B
C
Notes: Ok, now we are experts.
Just one small detail: Modern processes use 2 kinds of transistors.

## Slide 28: Logic Gates
Not
And
Or
Xor
Nand
Nor
Basic elements needed to implement combinational logic

## Slide 29: Logic NOT (Inverter)
Notes: Certain teenagers and politicians implement this very well.

## Slide 30: NAND Gates

## Slide 31: Part III: Truth Tables and Boolean algebra

## Slide 32: Processor Design
Combinatorial Logic
  Logic, arithmetic
  Hardware!
Sequential Logic
  Memory
  Time: do this, then that
Datapath
  Implement instruction set
Control
  Telling each piece what to do
Pipelining
  Make it go fast!

## Slide 33: The Von-Neumann Model
Memory
Control Unit
I/O
ALU
Reg
File
PC
IR
Processing Unit
Notes: Insert von-neumann schematic here

## Slide 34: Logical Design of Digital Systems
Complex Combinational and Sequential networks (up to thousands of gates)
  Emphasis on combined datapath + Finite state machine designs for real time applications
Modern CAD tool usage (schematic entry, simulation, technology mapping, timing analysis, synthesis)
Logic Synthesis via Verilog
Modern implementation technologies such as Field Programmable Gate Arrays (FPGAs)

## Slide 35: Truth Table
The truth value of a statement is the classification as true or false which denoted by T or F
  In logic circuits, T is 1 and F is 0
The truth table lists all possible combinations of the individual statements as true or false, along with the resulting truth value of the compound statements.
Truth tables are an aide in distinguishing valid and invalid arguments.

## Slide 36: Truth Table for p and q
A conjunction is the joining of two statements with the word and
The number of rows in this truth table will be 4 (22).
  Since p has 2 values, and q has 2 values)
For p and q to be true, then both statements p, q, must be true.
If either statement or if both statements are false, then the conjunction is false.
p | q | p and q
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 37: Logic Gates: Truth Tables

## Slide 38: Truth Tables
0
How many Fs (4-input devices)?

## Slide 39: Number of Rows
If a compound statement consists of n individual statements, each represented by a different letter, the number of rows required in the truth table is 2n.

## Slide 40: Boolean Algebra
George Boole, 19th Century mathematician
  Early computer designers built ad hoc circuits
  Began to notice common patterns in their work: NOTs, ANDs, ORs, XORs, …
  Applied formal math to hardware design, logic minimization, …
The power of Boolean Algebra is that there’s a one-to-one correspondence between circuits made up of AND, OR and NOT gates and equations.

## Slide 41: Boolean algebra
Boolean algebra
  B = {0, 1}
  + is logical OR, • is logical AND
  ' is logical NOT
All algebraic axioms hold

## Slide 42: Laws of Boolean Algebra
Identity: X + 0 = X Dual: X • 1 = X
Null: X + 1 = 1 Dual: X • 0 = 0
Idempotent: X + X = X Dual: X • X = X
Involution: (X')' = X
Complementarity: X + X' = 1 Dual: X • X' = 0
Commutative: X + Y = Y + X Dual: X • Y = Y • X
Associative: (X+Y)+Z=X+(Y+Z) Dual: (X•Y)•Z=X•(Y•Z)
Distributive: X•(Y+Z)=(X•Y)+(X•Z) Dual: X+(Y•Z)=(X+Y)•(X+Z)
Uniting: X•Y+X•Y'=X Dual: (X+Y)•(X+Y')=X

## Slide 43: Laws of Boolean Algebra
Absorption: X+X•Y=X Dual: X•(X+Y)=X
Absorption (#2): (X+Y')•Y=X•Y Dual: (X•Y')+Y=X+Y
de Morgan's: (X+Y+...)'=X'•Y'•... Dual: (X•Y•...)'=X'+Y'+...
Duality: (X+Y+...)D=X•Y•... Dual: (X•Y•...)D=X+Y+…
Multiplying & factoring: (X+Y)•(X'+Z)=X•Z+X'•Y
  Dual: X•Y+X'•Z=(X+Z)•(X'+Y)
Consensus: (X•Y)+(Y•Z)+(X'•Z)= X•Y+X'•Z
  Dual: (X+Y)•(Y+Z)•(X'+Z)=(X+Y)•(X'+Z)

## Slide 44: Proving theorems
Example 1: Prove the uniting theorem: X•Y+X•Y'=X
  Distributive X•Y+X•Y' = X•(Y+Y')
  Complementarity = X•(1)
  Identity = X
Example 2: Prove the absorption theorem: X+X•Y=X
  Identity X+X•Y = (X•1)+(X•Y)
  Distributive = X•(1+Y)
  Null = X•(1)
  Identity = X

## Slide 45: DeMorgan’s Law:
AND and OR are interchangeable:
  E.g. realize AND with OR (and a few inverters, NOT’s)
Notes: 160Mflops, how fast is this? … my laptop is 100x faster!

## Slide 46: Binary Addition
A |  | 0 | 1 | 1 | 0
B | + | 0 | 1 | 1 | 1
S = A+B |  | 1 | 1 | 0 | 1
Binary addition is just like decimal addition
0
1
1
Carry

## Slide 47: Part IV: Algebraic Simplification

## Slide 48: Boolean Algebraic Simplification Example
Notes: Do on black board
First write truth table
Then minimize and check truth table
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = 1
= a + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 0 1 1

## Slide 49: Boolean Algebraic Simplification Example
Boolean Algebra also great for circuit verification Circ X = Circ Y? use Boolean Algebra to prove!

## Slide 50: Boolean Algebraic Simplification Example

## Slide 51: Canonical forms (1/2)
Sum-of-products
(ORs of ANDs)

## Slide 52: Canonical forms (2/2)

## Slide 53: Boolean Minimization
Reduce a Boolean equation to fewer terms - hopefully, this will result in using less gates to implement the Boolean equation.
Pencil-Paper: Algebraic techniques, K-maps or
Automated: Many powerful algorithms exist
A B C F 0 0 0 0 0 0 1 0 0 1 0 0 0 1 1 1 1 0 0 0 1 0 1 1 1 1 0 1 1 1 1 1
F = A’BC + AB’C + ABC’ + ABC
F = BC + AC + AB
Find Boolean adjacencies to minimize equation; eliminate redundant term

## Slide 54: K- maps
Graphical Aid for minimization - used to visualize Boolean adjacencies
A B C F 0 0 0 0 0 0 1 0 0 1 0 0 0 1 1 1 1 0 0 0 1 0 1 1 1 1 0 1 1 1 1 1
BC
00
01
11
10
0
A
1
0
0
0
1
0
1
1
1
BC
00
01
11
10
0
A
1
0
0
0
1
0
1
1
1
F = BC + AC + AB